	Relaxation and forcing circuit
in palette	| vectorized |

in diagram
The unit implements the mathematical representation for a circuit, the dynamics of which can be described through the ordinary differential equation (ODE) appearing as follows: / T_{2,i} cdot {{dy_i(t)} over {dt} } + y_i(t) ~=~ T_{1,i} cdot {{du_i(t)} over {dt} } + u_i(t) , / where u_i(t) is for i-th element of unit input signal, T_{1,i} ,~T_{2,i} are for elements of vectors of time constants, y_i(t) is for element of unit output signal. / With zero initial conditions assumed and for scalar input signal, the dynamics of the unit can be represented through the following transfer function: / W(s) ~=~ {T_1 cdot s + 1} over {T_2 cdot s + 1} . / Dimensions of input and output signals, and vectors of time constants shall be the same. / Properties: / Time constant T1 – vector of time constants T_1 in seconds. / Time constant T2 – vector of time constants T_2 in seconds. / Initial conditions – vector of initial values y_i(0) of the unit output. / Note: by default the unit implements the “relaxation forcing” of scalar input signal.