	Inertial-differentiating element
in palette

in diagram
The unit is vectorized and implements a mathematical model of the element, which dynamics can be described via a linear ordinary differential equation (ODE) as follows : / T_i cdot y_i ' ( t ) +y_i ( t ) =k_i cdot x_i ' ( t ) , / where x_i(t) is for the i-th element of input signal to the unit, T_i is for an element of constant time vector, k_i is for an element of the amplification factors vector, y_i(t) is for an element of the unit output signal. / In case of zero initial conditions the dynamics of the unit can be represented via the following transfer function: / W \( s \) ={k cdot s} over {T cdot s + 1} , / that is why the pictogram of the unit has the view of a transfer function of a inertial-differentiating element. / The dimensions of input, output and factors vector signals shall coincide. / Mandatory condition: T_i <> 0 . / Properties: / Time constants – are the vector of time constants T_i in seconds. / The initial conditions – are the vector of initial values y_i(0) for unit output value. / Note: by default the unit properties are set for the scalar input signal.