	Limited Integrator
in palette

in diagram
The unit is vectorized and implements a mathematical model of the element, which dynamics can be described via a linear ordinary differential equation (ODE) as follows: / y_i'(t) = k_i cdot x_i(t) , / in case of any limitations available for the output signal value: / y_min <= y_i(t) <= y_max , / where x_i(t) is for the i-th element of input signal to the unit, k_i is for the element of the vector of the amplification factors, y_i(t) is for the element of the unit output signal. / The unit integrates (within the limits) the input signal that is why the pictogram of the unit has the view of transfer function of ideal integrator with “the addition” of “equal to or less than” symbol. / The dimensions of input, output and vectors of the coefficients must be the same.cide. / Properties: / The amplification factors – the vector of the factors k_i the input value is multiplied by. / The initial conditions – the vector of initial values y_i(0) for unit output value. / Minimum value – the minimum output value y_min . / Maximum value – the maximum output value y_max . / Note: by default the unit integrates the scalar input signal.