	Discontinuity improvement
in palette	| vectorized |

in diagram
The unit performs a forced variation of integration step, when value of input signal is crossing a preset value. At the same time 1 is generated at the unit output if the transfer condition is fulfilled. / Properties: / Cross-over level – vector of values for every element of the input vector, whereby the integration step correction occurs. / Transfer direction indicator (1,-1) – vector of direction flags for transfer being improved for every element of input vector: -1 – up-transfer, 1 – down- transfer. / Temporal transfer accuracy – vector of transfer accuracy for every element of input vector. / Unit output dimension is equal to the input dimension. At every of the output elements 1 is generated if the transfer-over-value condition is fulfilled.