	State variables
in palette	| vectorized |

in diagram
The unit implements the description of multi-dimensional linear dynamic system in the matrix form: / left lbrace stack{ alignl {dx(t)} over {dt} = A cdot x(t) + B cdot u(t), # alignl ~y(t) = C cdot x(t) + D cdot u(t); } right none / where A,~B,~C,~D are for matrices: for the system, input, output and bypass correspondingly; x(t) is for vector of state variables (with dimension [N_x] ); u(t) is for input vector (with dimension [N_u] ); y(t) is for output vector (with dimension [N_y] ). / Dimension of matrix A ~ - ~ [N_x times N_x] . / Dimension of matrix B ~ - ~ [N_u times N_x] . / Dimension of matrix C ~ - ~ [N_x times N_y] . / Dimension of matrix D ~ - ~ [N_u times N_y] . / Note: the 1st number in square brackets is for the number of columns, the 2nd number is for the number of lines. / Mandatory condition: N_x >= N_y . / Unit input and output – vector signals (with dimensions [N_u] and [N_y] correspondingly). / Properties: / Number of state variables – N_x . / Number of input effects – N_u . / Number of outputs – N_y . / Matrix A(Nx*Nx). / Matrix B(Nu*Nx). / Matrix C(Nx*Ny). / Matrix D(Nu*Ny). / Initial conditions (Nx) – vector of initial conditions with dimension [N_x] .