	Exponent Function
in palette

in diagram
The unit is vectorized and returns the output value calculated as per the formula: / y(t) ~=~ a cdot exp(b cdot x(t) + c) ~=~ a cdot e^{b cdot x(t) + c} , / where a,~b,~c are exponential transformation coefficients, x(t),~y(t) are unit input and output signals. / Properties: / Amplification factor – the coefficient a . / Reverse time constant – the coefficient b . / Shift – the coefficient c . / The properties can be vectors, which dimensions shall be equal to the input dimension; in this case there will be a vector at the output.