	Arc cosine
in palette

in diagram
The unit is vectorized and returns the output value calculated as per the formula: / y(t) = a cdot arccos(%omega cdot x(t) + f) , / where a,~%omega,~f are for amplitude, circle frequency and phase, / x(t),~y(t) are for input and output signals. / Mandatory condition: abs {%omega cdot x(t) + f} ~<=~ 1 . / Properties: / Amplitude – the coefficient a . / Frequency – the coefficient %omega . / Phase – the coefficient f . / The properties can be vectors, which dimensions shall be equal to the input dimension; in this case there will be a vector at the output.