	Arc Tangent
in palette

in diagram
The unit is vectorized and returns the output value calculated as per the formula: / y(t) = a cdot arctg(%omega cdot x(t) + f) , / where a,~%omega,~f are for amplitude, circle frequency and phase, / x(t),~y(t) are for input and output signals. / Properties: / Amplitude is coefficient a . / Frequency is coefficient %omega . / Phase is coefficient f . / The properties can be vectors, which dimensions must be equal to the dimension of the input vector signal, in this case, the output will also be a vector signal.