	Exponential Function of Variable Amplitude
in palette

in diagram
The unit is vectorized and returns the output value calculated as per the formula: / y(t) = a cdot u_1(t)^{b cdot u_2(t)} , / where a is for the multiplier (i.e., amplitude or amplification coefficient), / b is for coefficient to the power, u_1(t),~u_2(t) are for 1st and 2nd input signals of the unit. / Mandatory condition: u_1(t) > 0 . / Properties: / Multiplier in the function a*(u1^(b*u2)) is coefficient a . / Coefficient to the power is coefficient b . / The properties can be vectors, which dimensions must be equal to the dimension of the input vector signal, in this case, the output will also be a vector signal.