	NOT Operator
in palette

in diagram
The unit is vectorized and implements the logical NOT operation: / y(t) = left lbrace stack{ alignl 1, ~ if ~ u(t) = 0; # alignl 0, ~ if ~ u(t) = 1; } right none , / where y(t) is for unit output signal, u(t) is for input signal. / Properties: any properties are not required for operation of the unit. / Notes: / In case an input signal is not logical one (0 or 1) but presents an integer signal then all non-zero signals will be considered by the unit as equal to one (True). There can only be either 0 or 1 at the unit output. / In “SimInTech” Software system the logical one (True) is equal to 1, the logical zero (False) is equal to 0.