	Relay with non-sensitivity zone
in palette

in diagram
The unit is vectorized and implements the transformation of input signals by means of unified non-linear static characteristic of “relay multivalued with non-sensitivity zone” type with different initial conditions as per the following algorithm: / y(t) = left lbrace stack{ alignl y_1, ~ if ~ x(t) < a_1 # alignl 0, ~ if ~ a_2 < x(t) < b_1 # alignl y(t - %DELTA t), ~ if ~ a_1 <= x(t) <= a_2, ~"or"~ if b_1 <= x(t) <= b_2 # alignl y_2, ~ if ~ x(t) > b_2} right none , / where x(t) is for the vector of input signals; y(t) is for the vector of output signals; %DELTA t is for previous time step of integration; a_1 , a_2 , b_1 , b_2 , y_1 , y_2 are for parameters of static characteristics. / In case of “overlap” of return zones the switch-over process is determined considering the previous sate of the relay. / Properties: / Switch-over lower limit – a – the minimum input value whereby the output value is equal to the lower value. / Non-sensitivity zone lower limit – a_2 . / Non-sensitivity zone upper limit – b_1 . / Switch-over upper limit – b_2 – the maximum input value whereby the output value is equal to the upper value. / Function lower value – y_1 – the minimum value at the unit output. / Function upper value – y_1 – the maximum value at the unit output. / Initial conditions (0;1) – the initial state of the relay: 0 – off, 1 – on. / Note: in order to implement the vector processing any signals to be transformed shall be “compressed” in a vector input signal by means of a typical Multiplexer unit.