	Ideal transport delay
in palette	| vectorized |

in diagram
The unit is vectorized and implements the mathematical representation for a circuit the dynamics of which can be described via the linear equation (LE) with a delay: / y_i(t) ~=~ u_i(t - T_i) , / where u_i(t) is for the i-th element of the unit input signal, u_i(t-T_i) is for the value of the i-th element of the input signal stored in the unit T_i seconds back relative to current simulation time; T_i is for an element of the vector of delay times, y_i(t) is for an element of the unit output signal. / With zero initial conditions the unit dynamics can be represented via the following transfer function (for the scalar variant of signal): / W(s) ~=~ e^{-T cdot s} , / thus, the pictogram of this unit has an equivalent appearance. / Dimensions of signals of the input, output and vector of delay times shall be the same. / Properties: / Delay time – vector of delay times T_i in seconds. / Initial stack size – initial array size the unit input data are stored within. / Note: by default the unit implements a “delay” of a scalar input signal.