	Restricted derivatives
in palette

in diagram
The unit is vectorized and implements the numerical determination of a derivative with restricted output value module as per the following formula: / y_i(t) = min left [ {du_i(t)} over {dt}, A right ] , / at each time step as relation of incremented dynamic variable to time, where u(t) is for the vector of input signals, y(t) is for the vector of output signals. / Properties: / Initial conditions – the value of output vector at t=0 . / Derivative maximum value – A . / Note: in order to implement the vector processing any signals to be transformed shall be “compressed” in a vector input signal by means of a typical Multiplexer unit.