	Knee
in palette

in diagram
The unit is vectorized and implements the transformation of the vector of input signals by means of uniform non-linear static characteristic of “Knee” type as per the following algorithm: / y(t) = left lbrace stack{ alignl k_1 cdot u(t), ~ if ~ u(t) < u_0 # alignl k_2 cdot u(t), ~ if ~ u(t) >= u_0 } right none , / where u(t) is for the vector of input signals; y(t) is for the vector of output signals; / Properties: / K at x < 0 – the coefficient k_1 . / K at x > 0 – the coefficient k_1 . / Knee point – u_0 . / Note: in order to implement the vector processing any signals to be transformed shall be “compressed” in a vector input signal by means of a typical Multiplexer unit.