	Key-0
in palette

in diagram
The unit is vectorized and implements the function of controllable key as per the algorithm: / y(t) = left lbrace stack{ alignl y_0, ~ if ~ u(t) < K # alignl x(t), ~ if ~ u(t) >= K} right none , / where u(t) is for the vector of input signals, y(t) is for the vector of output signals, K is for the vector of “thresholds” (parameters of settings), y_0 is for the vector of unit output signals with input signals featuring lesser threshold values. / Properties: / Setting – the vector of “thresholds” K . / Subthreshold value – the vector of unit output signals y_0 (with input signals featuring lesser threshold values).