	Key-1
in palette

in diagram
The unit is vectorized and implements the function of controllable key as per the algorithm: / y_1(t) = left lbrace stack{ alignl u(t), ~ if ~ u(t) >= K # alignl y_0, ~ if ~ u(t) < K } right none newline y_2(t) = left lbrace stack{ alignl u(t), ~ if ~ u(t) < K # alignl y_0, ~ if ~ u(t) >= K } right none , / where u(t) is for the vector of input signals; / y_1(t) is for the vector of output signals at the 1st output port; / y_2(t) is for the vector of output signals at the 2nd output port; / K is for the vector of threshold values (settings) defining the conditions for overcommutation of signals at the unit output ports; / y_0 is for the vector of signals at the 1st output port of the unit with input signals featuring lesser threshold values K or the vector of signals at the 2nd output port of the unit with input signals featuring greater threshold values K . / Properties: / Setting – the vector of “thresholds” K . / Subthreshold value – the vector of signals y_0 at the 1st output port of the unit with input signals featuring lesser threshold values K or, correspondingly, the vector of signals at the 2nd output port of the unit with input signals featuring greater threshold values K .