	Key-6(t)
in palette	| vectorized |

in diagram
The unit implements the function of controllable key as per the algorithm: / y_{1,i}(t) = left lbrace stack{ alignl u_i(t), ~ "if" ~ t < T_{10,i}, # alignl Y_{10,i}, ~ "if" ~ t >= T_{10,i}; } right none newline y_{2,i}(t) = left lbrace stack{ alignl u_i(t), ~ "if" ~ t >= T_{20,i}, # alignl Y_{20,i}, ~ "if" ~ t < T_{20,i}; } right none / where u(t) is for the vector of output signals; / y_1(t),~y_2(t) are for vectors of output signals at the 1st and 2nd output ports; / Y_10 is for the vector of output signals at the 1st output port with t>=T_10 ; / Y_20 is for the vector of output signals at the 2nd output port with t<T_20 . / Properties: / First output setting – vector T_10 . / Second output setting – vector T_20 . / 1st vector initial value – vector Y_10 . / 2nd vector initial value – vector Y_20 . / Notes: / By default the unit generates scalar output signals. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.