	Integrator Key
in palette

in diagram
The unit implements the function of controllable key for integrating drive (of integrator or inertial-integrating element type) as per the following algorithm: / y(t) = left lbrace stack{ alignl u_1(t), ~if~ a_1 < u_2(t) < a_2 ,# alignl 0, ~if~ u_2(t) <= a_1 ~и~ u_1(t) <= 0, ~"or"~ u_2(t) >= a_2 ~"and"~ u_1(t) >= 0 , # alignl u_1(t), ~if~ u_2(t) <= a_1 ~и~ u_1(t) > 0, ~"or"~ u_2(t) >= a_2 ~"and"~ u_1(t) < 0; } right none / where u_1(t) is for signal at the 1st input port; / u_2(t) is for control signal to the unit 2nd input (from the integrator output, fitted behind the unit in series); / y(t) is for signal at the output port (at the integrator input); / a_1, a_2 are for threshold values (logical settings, as a rule, or, e.g. (conventionally) positions of lower and upper limit switches, correspondingly). / ATTENTION: integrator amplification coefficient K > 0 . / Properties: / Minimum value – the vector a_1 . / Maximum value – the vector a_2 . / Note: the considered unit transforms a scalar input signal only.