	Normally closed controllable key type 1
in palette

in diagram
The unit is vectorized and implements the function of controllable key as per the algorithm: / y(t) = left lbrace stack{ alignl x(t), ~ if ~ Control (t) = 0; # alignl 0, ~ if ~ Control(t) = 1;} right none / where x(t) is for unit input signal (or the vector of signals), y(t) is for unit output signal (or the vector of signals). / Control signal enters the unit from the top. In the process of calculation the image of the unit changes depending on the availability of a control signal: the key is normally closed, when a control signal is delivered the key is open: / Control = 0 Control = 1 / The unit is a submodel (assembly). For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / Properties: any properties are not required for operation of the unit.