	Normally open controllable key type 3
in palette

in diagram
The unit is vectorized and implements the function of controllable key as per the algorithm: / y_1(t) = left lbrace stack{ alignl 0, ~ if ~ Control (t) = 0; # alignl x_1(t), ~ if ~ Control (t) = 1;} right none newline y_2(t) = left lbrace stack{ alignl 0, ~ if ~ Control(t) = 0; # alignl x_2(t), ~ if ~ Control(t) = 1;} right none / where x_1(t), x_2(t) are for unit input signals (or vectors of signals), y_1(t), y_2(t) are for unit output signals (or vectors of signals). / Control signal enters the unit from the top. In the process of calculation the image of the unit changes depending on the availability of a control signal: the key is normally open, when a control signal is delivered the key is closed: / Control = 0 Control = 1 / The unit is a submodel (assembly). For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / Properties: any properties are not required for operation of the unit. / Notes: since the key (submodel) algorithm is implemented by means of “Multiplier” unit then, when a control signal different from 1 is delivered, a signal equal to the product of x_i(t) by the value of control signal will appear at the unit output.