	Multiplication of vector elements
In palette

In diagram
The unit is vectorized and implements the multiplication of all elements of input vectors. The output is a scalar value: / y(t) = a_1 cdot sum {u_{1,i}(t)} ~times~ a_2 cdot sum {u_{1,i}(t)} ~times~ ... , / where u_{1,i}(t), u_{2,i}(t), ... are for vectors of unit input signals (elements of vectors u_{1}(t), u_{2}(t), ... ), y(t) is for unit output signal, a_1 , a_2 , ... are for input weight factors. / Properties: / Input weight factors are numerals a_1,a_2,... the values of input ports of the unit are multiplied by. Number of input ports of the unit is equal to the dimension of this parameter.