	Reproducer
In palette

In diagram
The unit is vectorized and implements the multiplication of an input signal (or elements of input signal vector) by the column-vector (or column-vectors) of amplification coefficients. / If there is a scalar signal at the input then the unit realizes the function of multi-channel amplification circuit: / vec{y}(t) = vec{k} cdot x(t) or y_i(t) = k_i cdot x(t) , / where x(t) is for input signal (scalar), k_i is for column-vector element of amplification circuit s vec{k} , y_i(t) is for element of output vector signal vec{y}(t) . / If a vector signal is delivered to the unit intput then column-vectors shall be set as reproduction constants. Number of column-vectors of reproduction constants should not necessarily be equal to the dimensionality of input vector signal. At that the unit implements the transformation of input vector signal as per the algorithm: / vec{x}(t) = [x_1(t), x_2(t)...x_N(t)] ~ rightarrow ~ left [ stack { x_11(t),...x_1N(t) # x_21(t),...x_2N(t) # ... ... ... # x_M1(t),...x_MN(t) } right ] ~ rightarrow ~ newline ~ rightarrow ~ vec{y}(t) = [x_11(t),...x_1N(t),...x_M1(t),...x_MN(t)] / Input vector vec{x}(t) interpreted as a line-vector is transformed to a matrix of [N times M] size, each column of which is derived from an input vector element as a result of its multiplication by a corresponding column-vector of amplification coefficients. Then the matrix is read out line-by-line and obtained vector vec{y}(t) is delivered to the unit output. / Properties: / Reproduction constants - vector(s) of reproduction constants. / Example for filling the dialog window: / Let us assume that input signal vec{x}(t) = [x_1(t),x_2(t)] is 2-cored one (N = 2). / The given vector shall be reproduced trice (M = 3), at the same time signal at the 1st “core” of input vector shall be amplified two-, three- and five-fold, while the signal at the 2nd “core” of the input vector shall be amplified four-, two- and seven-fold, correspondingly. / Numerical representation of the setting of amplification coefficients is: [[2,3,5], [4,2,7]] / Then the output vector will have the value: vec{y}(t) = [ 2 cdot x_1(t),~4 cdot x_2(t), ~ 3 cdot x_1(t),~2 cdot x_2(t), ~ 5 cdot x_1(t),~7 cdot x_2(t) ]