	Stop block
in palette	| scalar |

in diagram
The unit performs the procedure for stopping the calculation or temporarily interrupting the calculation in case the input signal value enters a preset range: / left ldline stack { alignl "if" ~ u(t) >= u_min ~ "and" ~ u(t) <= u_max , # alignl "then" ~ "stop" ~ "calculation" ~"and"~ "show" ~"Message" } right none / where u(t) is for input scalar signal; u_{min}(t) , ~ u_{max}(t) are for stop-interval margins. / Properties: / Left margin of stop-interval - number u_min . / Right margin of stop-interval – number u_max . / Message on stopping the calculation – text “Msg” displayed for the User in case the signal enters into the stop-interval and, thus, on stopping the calculation. / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Left margin of stop-interval [124] / Right margin of stop-interval [2000] / Message on stopping the calculation Power exceeded 124% / Named definition of properties: / Name Value / Left margin of stop-interval [a1] / Right margin of stop-interval [a2] / Message on stopping the calculation Stop of calculation / Mixed definition of properties: / Name Value / Left margin of stop-interval [100] / Right margin of stop-interval [a_max] / Message on stopping the calculation Stop of calculation / Notes: / The unit processes the scalar input signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.