	Piecewise-constant
in palette	| vectorized |

in diagram
The unit generates a random piecewise-constant (multistep) output signal, which is superposition of step effects. / Properties: / Time intervals array – t – time intervals array, in seconds. / Values array – y – output signal values array. / The properties are matrices wherein vector of times or values is to be set up in every line for correspondent element of the output vector. / Examples of filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Time intervals array [10,10,10,170] / Function value [0,1,0,1] / Named definition of properties: / Name Value / Time intervals array [6#t1] / Function value [y1,y2,y1,y3,y1,y4] / Mixed definition of properties: / Name Value / Time intervals array [100,t2,100,100,150,100] / Function value [y1,y2,y3,y4,y5,y6] / Vector definition of properties (two-lined matrix): / Name Value / Time intervals array [[t1,t1,t1,t1,t1,t1],[t1,t1,t1,t1,t1,t1]] / Function value [[y1,y2,y3,y4,y5,y6],[1,2.5,3,4,3,1]] / Notes: / By default the unit generates a scalar output signal. / Named properties are set up as local variables of model (or submodel) in Parameters tab or as global signals of the project via Graphics → Signals main menu option.