	Integrator with changeable initial conditions
In palette

In diagram
The unit is vectorized and implements the integration of input signal: / y_i(t) = {int from {t_1} to {t_2} u_i(t)dt} , / where u_i(t) are for elements of input signal vector, y_i(t) are for elements of output signal vector, are for time intervals of switch-over of initial conditions. / The unit has 3 input ports and, when positioned left-to-right: / 1st input port (top-left) – integrated vector signal; / 2nd input port (middle-left) – control signal; / 3rd input port (bottom-left) – vector of new initial conditions. / If t = t_1 new initial conditions are established and if t_1 < t < t_2 input vector signals are integrated with these new initial conditions. / If t = t_2 a next alteration of initial conditions takes place, and if t > t_2 next stage of integration with new initial conditions is carried out till a new next alteration of initial conditions. / Change-over of initial conditions takes place only in case the control signal changes over from one value, e.g., form 1, to another one, e.g., 2, or vice versa, from 2 to 1. / Dimensions of integrated signal and signal of initial conditions shall be the same, e.g., if the input vector is “three-cored” then the signal of initial conditions is also “three-cored”. / Properties: / Number of variables of the status is dimensions of the output vector. / 1st value of control signal. / 2nd value of control signal. / Notes: / By default the considered unit realizes the integration of scalar input signal. / It is recommended (although not mandatory) to use the values of control signals 0 and 1, since their generation is easily realized by typical logic units.