	Residual energy release
in palette	| scalar |

in diagram
If the nuclear reactor operates in proximity to the nominal mode then neutron kinetics equations only can be used for its (neutron or thermal) power calculation since in this case relative neutron power values (normalized against nominal neutron power) and relative thermal power values (normalized against nominal thermal power) are approximately equal to each other: / {N_neutr(t)} over {N_neutr^{nom}} simeq {N_therm(t)} over {N_neutr^{nom}} ~rightarrow~ N_therm(t) = N_therm^{nom} cdot tilde{n}(t) and {N_neutr(t)} = N_neutr^{nom} cdot tilde{n}(t) / If the reactor neutron power has drastically changed, then, when calculating the thermal power, one shall consider the effect of residual energy release. / Relative neutron power calculated by means of Neutron Kinetics unit is delivered to the Residual Energy Release unit, at the same time 1 shall be set in Normalizing line of the Neutron Kinetics unit dialog window. / Prehistory of reactor operations appearing as a superposition of step functions shall be set in the Residual Energy Release unit dialog window. / Example of the use of the Residual Energy Release unit is shown in Figure 1. / Figure 1 — Rod drop / Typical Amplifier unit normalizes the reactor thermal power, while inscription 1/1.0658 under the unit “informs” that by the moment of emergency situation an additional contribution to the residual energy release thermal power is 6.58%. / Rod drop low / Classic kinetics / Thermal power / and residual / energy release