	Data import from exchange file
in palette	| vectorized |

in diagram
The unit is intended to read out data from binary exchange file. Read-out is implemented with a preset interval. Number of read-out signals is equal to the sum of output dimensions. / Exchange file format is as follows: / [data number N – int32][value 1 – real 8]….[value N – real 8] / Unit properties: / Output dimensions array – dimensions of unit outputs. / Output initial values array – dimensions of outputs with t=0 if property “Initial state = From array”. / Import data file – relative path to the data exchange file. / Synchronize data exchange – if the flag is set to “Yes” the unit automatically delays the calculation, if number of data in the exchange file = 0. After reading out this unit will record the number of exchange file data as = 0 / Data exchange interval – an interval the data is read out from the exchange file. / Stop against flag on exchange file – if the flag is set to “Yes” then the unit automatically stops the calculation, if number of data in the exchange file < 0. / Initial state – a flag indicating where initial values for unit outputs should be taken from. / Waiting interval – interval of delay in milliseconds during synchronization of the unit.