	Polyline steady-state characteristic
In palette

In diagram
The unit is vectorized and implements the transformation of the vector of input signals by means of a unified single-value non-linear steady-state characteristic a random appearance, i.e., a fitted piece-broken curve: / If input signal is less than x_1 or more than x_n then a correspondent constant value is formed at the unit output: / y_i(t) = left lbrace stack{ alignl y_1, ~ "if" ~ x_i(t) < x_1 # alignl y_n, ~ "if" ~ x_i(t) > x_n } right none , / where x(t) is for the vector of input signals; y(t) is for the vector of output signals. / Properties: / Vector of argument values – array of arguments x_j . / Vector of function values – array of output signal values y_j . / Note: to implement the vector processing any signals to be transformed shall be “compressed” in a vector input signal by means of a typical Multiplexer unit.