	Variable transport delay
in palette	| vectorized |

in diagram
The unit implements the solution of the transport transfer equation (system of equations) for disintegrating scalar substance appearing as: / {{dy_i(x,t)} over {dt} } + u_i(t) cdot {{dy_i(x,t)} over {dx} } ~=~ - %lambda_i cdot y_i(x,t) / on the assumption that the velocity of scalar substance transfer is constant within the limits of a portion for each moment of time with boundary conditions / y_i(0,t) = u_i(t) / and initial conditions / y_i(x,0) = y_{0,i}(x),~x in {[0,L]} . / In the equation y_i(t) is for transferable scalar substance, u_i(t) is for transfer velocity, L is for length of scalar substance transport (transfer) portion, x is for spatial coordinate. / After entering the dimensionless spatial coordinate z = x over L and scalar substance instantaneous transfer time within the limits of portion %tau_i(t) = L over {u_i(t)} the equation will appear as follows: / {{dy_i(z,t)} over {dt} } + {1 over %tau_i(t)} cdot {{dy_i(z,t)} over {dz} } ~=~ - %lambda_i cdot y_i(z,t) , / while the initial conditions appear as : y_i(z,0) = y_{0,i}(z),~z in {[0,1]} . / Mandatory condition: / %tau_i(t) > 0 . / The unit has 2 input and 2 output ports. / A signal correspondent to the scalar substance value at the input to the transport portion / y_i(0,t) = u_i(t) is delivered to the 1st input port. / A signal correspondent to the scalar substance transfer instantaneous time of within transport portion %tau_i(t) is delivered to the 2nd input port. / A signal correspondent to the scalar substance value at the output from transport portion is y_i(1,t) generated at the 1st output port. / A signal correspondent to the duration value of scalar substance “mark” staying within transport portion T_i(t) is generated at the 2nd output port. / Properties: / Vector of disintegration constants – vector of coefficients %lambda_i . / Initial stack size - initial size of an array for temporary storage of unit data. / Note: by default the unit implements variable and transport delay for scalar input signal.