	Clearance
In palette

In diagram
The unit is vectorized and implements the transformation of the vector of input signals by means of a unified non-linear static curve of “Clearance” type with different initial conditions as per the following algorithm: / y(t) = left lbrace stack{ k cdot (x(t)-b), ~ "if" ~ x(t) ~>~ { {y(t- %DELTA t)} over {k} + b} ; # k cdot (x(t)+b), ~ "if" ~ x(t) ~<~ { {y(t- %DELTA t)} over {k} - b} ; # y(t- %DELTA t), ~ "if" ~ { {y(t- %DELTA t)} over {k} - b} ~ <= ~ x(t) ~ <= ~ { {y(t- %DELTA t)} over {k} + b} ; } right none / where x(t) is for the vector of input signals, y(t) is for the vector of output signals, %DELTA t is for a previous time step of integration. / Properties: / Half of clearance zone width – b ; / Amplification coefficient – k ; / Initial conditions – vector of initial conditions y(0) . / Note: to realize the vector processing any signals to be transformed shall be “compressed” in a vector input signal by means of a typical Multiplexer unit.