	Free play
In palette

In diagram
The unit is vectorized and implements the transformation of the vector of input signals by means of a unified non-linear static curve of “Free play” type with different initial conditions as per the following algorithm: / y(t) = left lbrace stack{ y_1, ~"if"~ x(t) ~<=~ { {y_1} over {k} - b} ; # y_2, ~"if"~ x(t) ~>=~ { {y_2} over {k} + b} ; # k cdot (x(t)-b), ~"if"~ { {y(t- %DELTA t)} over {k} + b} ~<~ x(t) ~<~ {{y_2} over {k} + b} ; # k cdot (x(t)+b), ~"if"~ { {y_1} over {k} - b} ~<~ x(t) ~<~ { {y(t- %DELTA t)} over {k} - b} ; # y(t- %DELTA t), ~ "if" ~ { {y(t- %DELTA t)} over {k} - b} ~ <= ~ x(t) ~ <= ~ { {y(t- %DELTA t)} over {k} + b} . } right none / where x(t) is for the vector of input signals; y(t) is for the vector of output signals, %DELTA t is for a previous time step of integration. / Properties: / Half of clearance zone width – b . / Amplification coefficient – k . / Initial conditions – vector of initial conditions y(0) . / Lower value of the function – y_1 . / Upper value of the function – y_2 . / Note: to realize the vector processing any signals to be transformed shall be “compressed” in a vector input signal by means of a typical Multiplexer unit.