	Minimum at inputs
In palette

In diagram
The unit is vectorized and performs the elementwise calculation for the minimum or maximum of current input values: / y_i(t) = min left ( u_{1,i}(t), ~ u_{2,i}(t), ~ ... right ) or y_i(t) = max left ( u_{1,i}(t), ~ u_{2,i}(t), ~ ... right ) , / where i is for the vector element No., u_1(t) is for the first input vector, u_2(t) is for the second input vector, y(t) is for the output vector. / Properties: / Number of ports – number of unit input ports; / Type of operation – type of operation: minimum or maximum. / Note: to realize the vector processing any signals to be transformed shall be “compressed” in a vector input signal by means of a typical Multiplexer unit.