	Minimum over all vector elements
In palette

In diagram
The unit is vectorized and performs the elementwise calculation for the minimum or maximum of elements of the input vector (input vectors): / y(t) = min left ( u_{1,i}(t), u_{2,i}(t), ... right ) or y(t) = max left ( u_{1,i}(t), u_{2,i}(t), ... right ) , / where i is for element of the vector, x_{j,i}(t) are for elements of all input signals, for output signal, scalar. / Properties: / Number of ports – number of ports in the unit; / Type of operation – type of operation: minimum or maximum. / Note: to realize the vector processing any signals to be transformed shall be “compressed” in a vector input signals by means of a typical “Multiplexer” unit.