	Level quantizer
In palette

In diagram
The unit is vectorized and performs the quantization of a signal over discrete levels with a preset level step. The algorithm of operation of the unit is as follows: / y_i(t) = d_i cdot sign left ( u_i(t) right ) cdot floor left (abs{{u_i(t)} over {d_i}} + 0.5 right ) , / where u_i(t) is for i-th element of input signal to the unit, d_i is for i-th element of the vector of level quantization steps, floor is for the rounding function down to the lesser number, sign is for the sign function, y_i(t) is element of output signal from the unit. / Properties: / Quantization step – is the vector vec {d} of quantization steps over each element of the input vector. Dimensions of the parameter shall coincide with dimensionality of the input vector. / Notes: / By default the unit implements the processing of scalar input signal. / When using the considered unit, one can easily realize the mode of signal processing in analog-digital converter (ADC).