	Solution of a system of linear equations
in palette	| vectorized |

in diagram
The unit implements the procedure for solution of a system of linear equations appearing as follows: / A cdot x(t) = u(t) ~dlrarrow~ left lbrace stack{ alignl a_11 cdot x_1(t) + a_12 cdot x_2(t) +~...~+ a_1n cdot x_n(t) ~=~ u_1(t); # alignl a_21 cdot x_1(t) + a_22 cdot x_2(t) +~...~+ a_2n cdot x_n(t) ~=~ u_2(t); # alignl . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . # alignl a_n1 cdot x_1(t) + a_n2 cdot x_2(t) +~...~+ a_nn cdot x_n(t) ~=~ u_n(t); } right none / where A is for matrix of coefficients; x(t) is for vector of solutions; u(t) is for vector of right parts. / The unit has two vectorized input ports: / 1st input port – for entering the matrix A represented as a vector of coefficients, when unpacking the matrix in linewise manner. / 2nd input port – for entering the vector u(t) (vector of right parts). / The unit has one vector output port intended for outputting the vector x(t) (vector of solutions). / Vector signal dimension at the 1st input port shall be equal to n times n , where n is for the number of equations in the system, while dimensions of 2nd input port and output port signals are the same and equal to n . / Properties: / Number of equations – natural number n equal to the number of matrix lines (or columns) (i. e., dimension of matrix A ). / Example. / The following system of equations is to be solved: / left lbrace stack{ alignl 2 cdot x + 3 cdot y ~=~ 8; # alignl 5 cdot x - 2 cdot y ~=~ 1, } right none / which has an evident solution x=1, ~y=2 . / The figure below demonstrates a block diagram for this task solution. Typical Replicator units are used for generating input vector signals: / Note: the unit carries out the procedure for solution of linear algebraic equations after every successful completion of an integration step. / Solutions