	Flip matrix
in palette	| vectorized |

in diagram
The unit implements the procedure for square matrix flipping: / y(t) ~=~ A^T ~=~ left [ stack{ alignl a_11~ a_12 ~...~ a_1n # alignl a_21~ a_22 ~...~ a_2n # alignl . . . . . . . . . . . . . . . . . . # alignl a_n1~ a_n2 ~...~ a_nn } right ]^T ~=~ left [ stack{ alignl a_11~ a_21 ~...~ a_n1 # alignl a_12~ a_22 ~...~ a_n2 # alignl . . . . . . . . . . . . . . . . . . # alignl a_1n~ a_2n ~...~ a_nn } right ] , / where A is for matrix of coefficients; y(t) is for vector at the unit output. / The unit has one vectorized input port for inputting the matrix A represented as vector of coefficients, when unpacking the matrix in linewise manner. / The unit has one vector output port intended to output the flip result represented as vector of coefficients, when unpacking the flipped matrix in linewise manner. / Vector signal dimensions at input and output ports are the same. / Properties: / Matrix dimension – natural number n equal to the number of matrix lines (or columns).