	M from N
In palette

In diagram
It returns the logical one if number of the inputs, the value at which is equal to logical one, is greater than or equal to a preset number: / k=0 newline cycle ~ i=1...N: ~ if ~ (u_i(t) = 1) ~then~ k = k + 1 newline y(t) = left lbrace stack{ alignl 1, ~ if k >= M; # alignl 0, ~ if k < M; } right none , / where u_i(t) is for the scalar at the i-th input to the unit, y(t) is output logic signal, k is for the unit internal variable to calculate a number of input signals equal to one. / Properties: / Number of ports – is a number of input ports N . / Number of input True for actuation – is a number M of input signals equal to one, on achieving to which a logic one is generated at the output.