	Timing confirmation
In palette

In diagram
The unit is vectorized and implements the timing “delay” for a change of a type of output logic signal in case of a change of a type of a relevant logic signal in the vector of input signals. / It changes the output value in case the condition is fulfilled longer than a preset time. / Properties: / Vector of confirmation times. / Confirmation is required – it is a condition whereby the pulse is generated. / Output type – it is a type of unit output: regular or inverted.