	XOR
In palette

In diagram
The unit performs the elementwise XOR (EXCLUSIVE OR) operation for input signals. By default the unit realizes the operation for two input signals: / y(t) = left lbrace stack{ alignl 0, ~ if ~ u_1(t) = 1, ~"and" ~u_2(t) = 1;# alignl 1, ~ if ~ u_1(t) = 1, ~"and" ~u_2(t) = 0;# alignl 1, ~ if ~ u_1(t) = 0, ~"and" ~u_2(t) = 1;# alignl 0, ~ if ~ u_1(t) = 0, ~"and" ~u_2(t) = 0; } right none / where y(t) is for unit output signal (scalar), u_1(t),~u_2(t) are for input signals (scalars). / The algorithm of operation for a number of input signals exceeding two: / y(t) = left lbrace stack{ alignl 1, ~ if only one of ~u_i(t) = 1, ~"and" all the others~u_i(t) = 0;# alignl 0, ~ otherwise. } right none / Property: / Number of ports – Number of unit input signals is indicated here.