	Counter
In palette

In diagram
The unit is vectorized and implements the processing of the vector (counting of pulses) for active input signals as per one of the following algorithm variants: / Variant 1 (option Within the range): / In case in the process of simulation the value of any active signal in the vector of input signals enters the limits of a preset range [u_min ... u_max] numeral 1 will be added to the currently available reading of the counter. This means that the relevant element in the unit vector output signal will be incremented by 1: / y_i(t) = y_i(t- %DELTA t) + 1, ~ if ~ u_i(t)>u_min ~ и ~ u_i(t- %DELTA t)<=u_min newline y_i(t) = y_i(t- %DELTA t) + 1, ~ if ~ u_i(t)<u_max ~ и ~ u_i(t- %DELTA t)>=u_max , / where y(t) is for unit output vector signal, u(t) is for input vector signal. / Variant 2 (option Out of the range): / In case in the process of calculation the value of any active signal in the vector of input signals falls out of the limits of a preset range [u_min ... u_max] numeral 1 will be added to the currently available reading of the counter. This means that the relevant element in the unit vector output signal will be incremented by 1: / y_i(t) = y_i(t- %DELTA t) + 1, ~ if ~ u_i(t)>u_max ~ и ~ u_i(t- %DELTA t)<=u_max newline y_i(t) = y_i(t- %DELTA t) + 1, ~ if ~ u_i(t)<u_min ~ и ~ u_i(t- %DELTA t)>=u_min . / Properties: / Lower limit of non-sensitivity – u_min . / Upper limit of non-sensitivity – u_max . / Counter if the input – it is an indicator for variants of operation of the unit. The counter counts if input signal enters the field Within the range or Out of the range.