	Reset priority RS trigger
In palette

In diagram
The unit realizes the reset priority RS trigger , i.e., if the logic one level is available at R and S inputs then the output obtains the logic zero value. / y(t) = left lbrace stack{ alignl y(t- %DELTA t), ~ if u_S(t) = 0, ~ "and" ~u_R(t) = 0; # alignl 1, ~ if u_S(t) = 1, ~ "and" ~u_R(t) = 0; # alignl 0, ~ if u_R(t) = 1; } right none , / where y(t) is for unit input signal, y(t- %DELTA t) is for output signal value at a previous time step of integration, u_S(t), u_R(t) are for the first and second unit input signals (derived from Set and Reset, correspondingly). / Properties: / Initial conditions – initial output values. / Add an inverted output – indicates the availability of an inverted output. / Note: trigger (trigger system) is a class of electric devices capable to remain in one of two stable states for a long period of time and change the states under an action of external signals.