	2-D table from file
in palette	| vectorized |

in diagram
The unit executes 2-D interpolation of input arguments as per a specified table. / First input of the unit – argument value as per table lines. / Second input of the unit – argument value as per table columns. / The table has the following format: / <argument values as per columns> / <argument as per line 1> <function values> / <argument as per line 2> <function values> / …. / <argument as per line N> <function values> / Example: / 1 2 3 / 1 0.1 0.2 0.3 / 2 0.6 0.8 0.9 / Property: / Name of file with table – relative path to the table file.