	Fractional part
in palette	| vectorized |

in diagram
The unit implements the operation of separation of the fractional part of an input signal. / The fractional part is understood as a difference between the signal and its integral part. / The fractional part of a positive number is non-negative, while the fractional part of a negative number is non-positive (see the Figure): / Fractional part calculation algorithm: / y(t) ~=~ "frac" left [ u(t) right ] ~=~ u(t) - "int" left [ u(t) right ] , / where y(t) is for output signal, u(t) is for unit input signal. / In case of a vector input signal the unit implements the operation of separation of the fractional part for each element of the Integral part of linear function input vector value. / Properties: no properties are required for operation of the unit. Note: output signal dimension is always equal to the input signal dimension. / Fractional part of linear function