	Discrete variable conditions
in palette	| vectorized |

in diagram
The unit implements the description of multidimensional linear dynamic system in the matrix form: / left lbrace stack{ alignl x[k+1] ~=~ A cdot x[k] + B cdot u[k], # alignl y[k]~~~ ~=~ C cdot x[k] + D cdot u[k]; } right none / where A,~B,~C,~D are for the matrices: own, input, output and by-pass, correspondingly; x \[ k \] is for vector of variable conditions (with dimension [N_x] ); u[k] is for input vector (with dimension [N_u] ); y[k] is for output vector (with dimension [N_y] ). / Matrix dimension A ~ - ~ [N_x times N_x] . / Matrix dimension B ~ - ~ [N_u times N_x] . / Matrix dimension C ~ - ~ [N_x times N_y] . / Matrix dimension D ~ - ~ [N_u times N_y] . / Notes: / The 1st figure in the square brackets is the number of columns, the 2nd figure is the number of lines. / If the unit has 1 input and 1 output ( N_u=1,~N_y=1 ), D = 0 and, correspondingly, the 7th line – [0]. / Matrices A,~B,~C,~D , when “assembled”, form a “rectangular” with the dimension: of lines – (N_x+N_y) , of columns – (N_x+N_u) . / To ensure the correct operation of the unit the maximum step of integration shall be set up not higher than T/2 . In case the integration runs with a constant step, the step is recommended to be set up so that the sampling period would be multiple to the step of integration T = k cdot h , where k,~h are for the integer number and for the step of integration. / The unit input and output are vector signals (with dimensions [N_u] and [N_y] , correspondingly). / Properties: / Sampling period – unit calculation sampling period T . / Number of variable conditions - N_x . / Number of input actions – N_u . / Number of outputs – N_y . / Matrix A(Nx*Nx). / Matrix B(Nu*Nx). / Matrix C(Nx*Ny). / Matrix D(Nu*Ny). / Initial conditions (Nx) – vector of initial conditions with dimension [N_x] .