	Cross-correlation function
in palette	| scalar |

in diagram
The unit implements the calculation of correlation of two scalar input signals. Correlation function for values x and y is determined as follows: / %rho_xy(r %DELTA t) ~=~ {R_xy (r %DELTA t)} over { sqrt{R_xx(r %DELTA t) cdot R_yy(r %DELTA t)} } , / where R_xy = 1 over {N-1} cdot sum from {n=1} to {N-r} {x_n cdot y_{n+r}} –is for covariance function; / R_xx,~R_yy is for autocovariance functions for values x and y; / N is for size of sampling; / r=1...m,~m<N is for time shift; %DELTA t is for sampling period. / Cross-correlation function is calculated as per the following algorithm: / Implementations of values (two signals) x and y are divided into separate series with size N; moreover, N shall be an integral power of 2. Linear trends are deleted from signals, when required. / Each segment is added with N zeros. / X and Y discrete Fourier transformation for values x and y are calculated as per FFT method: / X(f,T) = %DELTA t left ( sum from {n=1} to {N-1} {x_n cdot e ^ {{-i cdot 2 %pi k n} over {N}}} right ) , newline Y(f,T) = %DELTA t left ( sum from {n=1} to {N-1} {y_n cdot e ^ {{-i cdot 2 %pi k n} over {N}}} right ) . / Double-sided cross-spectral density is calculated for values x and y: / S_xy = G_xy over 2 / Inverse discrete Fourier transform runs for sequence S_xy , which enables a biased estimation for covariance function R^s_xy . / Unbiased estimation for correlation function is calculated as per the formula: / %rho_xy(r %DELTA t) ~=~ {R^s_xy (r %DELTA t)} over { sqrt { sum from {i=1} to N (x_i)^2 cdot sum from {i=1} to N (y_i)^2 }} cdot { {N} over {N-r} } / The unit has 2 input ports and 2 output ports. / Input signals shall be scalar. / Signal at the 1st output port is vector of time shifts. / Signal at the 2nd output port is vector of correlation function values. / Dimensions of output signals are the same and equal to the size of series N. / Properties: / Size of series – value of this property determines the size of series in sampling. The size of series shall be an integral power of 2. / Calculation over the whole sampling (Yes or No) – if this property is No, then the cross-correlation function will be calculated by separate series. If this property is Yes, then the cross-correlation function will be calculated against an unlimited number of values; results of the calculation will be averaged for all series. / Sampling period – the value of this property determines the duration of a time interval between two subsequent read-outs of signal values at the unit input. If this property is 0 (zero), then the read-out is running with the period equal to the step of integration. / Delete linear trend (Yes or No) – if this property is Yes, then linear trends will be preliminarily subtracted from the array of accumulated input signal values.