	Correlation coefficient
in palette	| vectorized |

in diagram
The unit implements the calculation of correlation coefficient for two input signals. / Correlation coefficient is calculated as per the following formula: / r_xy ~=~ { sum from{i=1} to{n} { left [ { left ( {x_i - M(x)} right ) cdot left ( {y_i - M(y)} right ) } right ] } over sqrt { sum from{i=1} to{n} left [ { left ( {x_i - M(x)} right )^2 } right ] cdot sum from{i=1} to{n} left [ { left ( {y_i - M(y)} right )^2 } right ] } } / where n is for sampling volume (number of values), / x_i is for amount of the i-th value of the first input signal, / y_i is for amount of the i-th value of the second input signal, / M(x) is for mathematical expectation of the first signal, / M(y) is for mathematical expectation of the second signal. / Correlation coefficient demonstrates how much the dependence between two signals is. If signals are linearly dependent then correlation coefficient for module is 1. / The unit has 2 input ports and 1 output port. Input signals can be vectors; their dimensions shall be the same. Dimension of output signal is always equal to dimension of input signals. / Properties: / Size of series – value of this property determines the size of series in sampling. / Calculation over the whole sampling (Yes or No) – if this property is No, then the correlation coefficient will be calculated by separate series. If this property is Yes, then the correlation coefficient will be specified immediately after receiving a next new couple of signal values at the unit inputs. / Sampling period – the value of this property determines the duration of a time interval between two subsequent read-outs of signal values at the unit input. If this property is 0 (zero), then the read-out is running with the period equal to the step of integration.