	Kurtosis
in palette	| vectorized |

in diagram
The unit implements the calculation of kurtosis (forth moment) of input signal. / Kurtosis is calculated as per the following formula: / T ~=~ {{1} over {N}} cdot sum from{i=1} to {N} {left ( {x_i - M} over {%sigma} right )^4 - 3 } / where N is for sampling volume (number of values), / x_i is for value of the i-th sampling element, / M is for mathematical expectation for random value. / Kurtosis describes the deviation of the shape of frequency function curve from the normal probability law. This value is equal to 0 for the normal probability law. / The unit has 1 input port and 1 output port. Input signal can be vector. Dimension of output signal is always equal to dimension of input signal. / Properties: / Size of series – value of this property determines the size of series in sampling. / Calculation over the whole sampling (Yes or No) – if this property is No, then the kurtosis will be calculated by separate series. If this property is Yes, then the kurtosis will be specified immediately after receiving the next new signal value at the unit input. / Sampling period – the value of this property determines the duration of a time interval between two subsequent read-outs of signal values at the unit input. If this property is 0 (zero), then the read-out is running with the period equal to the step of integration. / Delete linear trend (Yes or No) – if this property is Yes, then linear trend will be preliminarily subtracted from the array of accumulated input signal values.