	Dynamic sampling
in palette	| vectorized |

in diagram
The unit executes the procedure for sampling an element from a vector as per an indicated number. / Algorithm for operation of the unit is as follows: / left ldline stack { alignl CYCLE ~ i = 1 ... n # alignl ~ ~ IF ~u_{1}(t) = i ~ THEN ~ y(t) = u_{2,i}(t); ~ EXIT THE CYCLE # alignl CYCLE TERMINATION } right none / where u_1(t) is for the first input scalar signal defining the number of an element to be sampled beginning with 1; u_{2,i}(t) is for the i-th element of the second input vector signal vec{u}_2(t) , from which the element is being sampled; n>=1 is for dimension of the second input, natural number. / Properties: / No properties are required for operation of the unit. Notes: / The unit generates a scalar output signal.