	LS-approximation
in palette	| vectorized |

in diagram
The unit is intended to approximate table functions using the Least Squares Method (LS method). The unit has three vector inputs and two vector outputs. The array of values of arguments for table functions with dimension N_pnt is applied to the first input. The array of values of table functions with dimension N_pnt times N_fun is applied to the second input (thus, approximation of several functions set up in the same points against an independent argument can be carried out at the same time). The array of points of arguments with dimension N_arg , in which the value of approximated functions is to be calculated, is applied to the third input. Value N_arg is defined by the input signal dimension. / Values of functions calculated after approximation in the points defined in the third input port are applied to the first unit output. The dimension of this output is equal to N_arg times N_fun . / Values of coefficients of polynomial approximants (in increasing order for powers) are applied to the second output. The dimension of this output is equal to (Order+1) cdot N_fun . / Properties: / Shape function: / 1. Polinomial a[m] cdot x^m , ~m = 0 ... Order. / 2. a[m] cdot sin(m cdot %pi cdot x), ~m = 0 ... Order. / 3. a[m] cdot (1- x) cdot x^m , ~m = 0 ... Order. / Approximation order – Order . / Number of points of approximation function – N_pnt . / Number of functions – N_fun .