	DC motor
In palette

In diagram
The unit implements a mathematical model of direct current motor (DCM) with independent excitation. / Control of unit dynamics: / left lbrace stack{ M_д(t) = k_м cdot i(t) , # (R + L cdot {{d} over {dt} }) cdot i(t) = { {u(t) - k_c cdot {{dq(t)} over {dt}}} } , # J cdot {{d^2 q(t)} over {dt^2}} = M_д(t) - M_в(t); } right none (1) / where u(t) is for voltage applied to the motor armature, V; / i(t) is for current in the motor armature circuit, А; / q(t) is for the motor shaft angle, rad; / M_д(t) is for torque developed on the motor shaft, N·m; / M_в(t) is for disturbing torque on the motor shaft, N·m; / k_c is for the counterelectromotive force coefficient; / k_м is for torque constant; / R is for resistance of the motor armature circuit, Ohm; / L is for inductance of the motor armature circuit, H; / J is for moment of inertia of the motor rotor, kg·m2 (in case of an absolutely rigid mechanical transmission without a free play the reduced moment of inertia shall be considered instead of the moment of inertia of the motor rotor (J + Jнi2),where Jн is for the load inertia). / The unit has 2 input and 3 output ports. / Input signals: / Moment M_в(t) . / Voltage u(t) . / Output signals: / Shaft angle q(t) , rad. / Angular velocity (frequency) of rotation q'(t) , rad/s. / Moment developed on the motor shaft M_д(t) , N·m; / The following can be additionally provided at the third output: / Current in the motor armature circuit i(t) , А. / Properties: / Rotor circuit resistance R , Ohm; / Rotor circuit inductance L , H; / Torque constant k_м ; / Counter-electromotive force coefficient k_c ; / Moment of motor rotor inertia J , kg·m2; / Initial motor shaft angle q(0) , rad; / Initial angular velocity (frequency) of motor rotation q'(0) , rad/s; / Initial current in armature circuits i(0) , А. / Additional output.